## Slide 1: The main event will begin soon. Please take your seat. Access the event program and music scores with this QR code =>

## Slide 2: Raindrops on a Tin Roof: Exploring the Cyberinet
Matthew A. Bardin - PHD Candidate
Louisana State University - Experimental Music & Digital Media
04/18/2023

## Slide 3: Augmented Instruments
What is the Cyberinet?

## Slide 4: What is an Augmented Instrument?
Augmented Instruments are any instrument that has been altered or enhanced from its base capabilities in some way.
This can be done in a variety of methods.
Augmentation methods can be any combination of manual, automatic, acoustic, or electronic.
Many modern augmentations include electronic components and sensors.
Reid, Sarah, Sithi-Amnaui, Sara, & Kapur. Ajay. (2018). Women who Build Things: Gestural Controllers, Augmented Instruments, and Musical Mechatronics. Proceedings of the International Conference on New Interfaces for Musical Expression, 178-183.

## Slide 5: Recent Eras of Augmented Instruments
Pre-20th Century
Completely acoustic.
Generally looking to improve an instrument or crate a new one
Brass Mutes
Expansion of instrument families
20th Century
Early electronics
Became more powerful as electronics and computers improved.
Prepared Piano
Amplification
21st Century (so far)
Largely Electronic.
Exploring new timbres and instrument functionality with new technology.
MIGSI Trumpet, SABRe, Overtone Violin, MataSax
Notes: Begin with the idea of improving the capabilities of instrument
Seeking new and altered timbres
Futurists seek to create and explore new sounds in music
Electrical alteration
Many new augmented instruments focus on this idea of improving an instruments’ features and timbres. Many of these include modern technology.

## Slide 6: Cybernetic + Clarinet
Notes: Cyberinet = Cybernetic + Clarinet

## Slide 7: What is Cybernetic About it?
Cybernetic: The science of communications and automatic control systems in both machines and living things – Oxford Dictionary
  Definition ca. 1948 from the Greek “Kubernetes” meaning captain, pilot, conductor, etc.
The Cyberinet is used to collect performance data and automatically control the audio processing and other electronic elements of an electroacoustic performance.

## Slide 8: So, what does that mean? What does the Cybernet do?
The Cyberinet is a sensor array designed to be easily adapted the instrument for electronic music without impeding the performance of the instrument.
The Cyberinet can still be used as a regular clarinet barrel while powered off.
Creates sound and control possibilities with minimal additional knowledge.
Components are all common-place and use standard pin spacings.
Notes: Explains statement from previous slide. This slide is more about technical bonuses.

## Slide 9: Why use this Instrument?
Easy to implement.
Does not reduce the Clarinet’s capabilities.
Can easily add harmonic capabilities to the Clarinet.
Intuitive controls.
Can be used by performers, composers, and programmers.
Notes: More practical/artistic

## Slide 10: Creating the Cyberinet

## Slide 11: OEM Components OEM Components are standardized to be compatible with each other.
The Cyberinet is comprised of a main unit and smaller secondary unit.
Main Unit:
1200mAh Li-Po battery to power the device.
TP-4056 Type C board. (controls the charging and power distribution)
MPU-6050 board. (6 axis gyroscope and accelerometer)
SDP-31 Qwiic Connect board. (differential air pressure/flow and temperature)
ESP-32 DEVKIT board. (microcontroller and transmitter)
Secondary Unit:
2 momentary switches with independently programmable LEDs.
Also, the Cyberinet has 2 programmable LEDs, which are not OEM.
Notes: Keep this slide short. Spend more time on the images slide.

## Slide 12
Version 1 Components
MPU 6050 (Gyro + Accelerometer)
Pushbuttons
0602 Size SMD LEDs
TP-4056 (Power Distribution)
ESP-32 Microcontroller
SDP-31 Differential Pressure Sensor

## Slide 13
Main Unit & Button Expansion Prototypes
Bottom
Top
Buttons
Original Prototype Socket Board
Notes: Big original hand made circuit board. Green is original printed version of the hand made circuit. Buttons are purple.

## Slide 14
Version 1 Final PCB Diagrams
Main Board
Button Expansion

## Slide 15: Future Optional add-ons
To further expand the functionality of the Cyberinet, multiple optional expansion units contain a variety of other sensors and can be utilized through the same expansion port. These include:
Microphone
Finger pressure sensors
Secondary movement sensor
Speaker
All of these are still in development, with the microphone closest to being functional.

## Slide 16: Music

## Slide 17: Puzzle of a Park (2023)
Written to utilize the optional button add-on.
Performer triggers the on-stage microphone & playback of recordings with a single button.
Functions similarly to a loop pedal.
  Allows performer to multi-track and harmonize with themselves.

## Slide 18
Puzzle of a Park opening page
Adam Cope- Cyberinet

## Slide 19: Assembling the Units

## Slide 20: Assembling the Unit
1:
Attach LEDs and Resistors (SMD Components) to the PCBs.
2:
Solder the USB-C and JST connectors. These are supported by the outer case.
3:
Solder the larger components directly to the PCBs. The microcontroller and SDP chip should be elevated with pin headers.
4:
Add the power switch. When done, connect the battery Glue/Sand as needed.

## Slide 21
Version 1 Final PCB Diagrams
Main Board
Button Expansion
Notes: Just a quick reminder about these components going onto the main PCB

## Slide 22
Version 1 with Button Board

## Slide 23: How the Cyberinet works

## Slide 24: Collects data
The Cyberinet’s .ino code and attached sensors manage the collection of the performance data.
SDP31: Measures differential air pressure between the inside and outside of the instrument. Small tubes connect to the sensor to facilitate this. Also measures temperature.
MPU6050: Measures performer movement in 6 axis.
Buttons: triggerable by the performer

## Slide 25
Data Collection Code
Notes: Each function collects and transmits data. Gyro has scaling for gravity and earth rotation. LED turns on to indicate transmitting

## Slide 26: Transmits wirelessly
The main unit’s ESP-32 board the transmitting as well as the data collection.
By utilizing the Arduino library “BluetoothSerial” the DEVKIT can transmit serial communications through a Bluetooth connection. The device name is “CyberinetV1X” and currently requires no password to connect.
These values can be read by any serial terminal program on the host device. The Max objects utilize an additional node script to receive the data more reliably.
Notes: Adds label to vale and transmits them as a pair. Can be read by anything that can receive serial data.

## Slide 27: Performer Opinions
We will take a few seconds to ask Adam about his thoughts with using the device.
He hasn’t been told about this.
What are your honest opinions on the usability, flexibility, and anything else you would like to mention?

## Slide 28: Music

## Slide 29: Ethereal Presence (2022)
Utilizes gyroscope and airflow sensors.
As the performer moves, the position of their instrument changes the pitch content of the accompaniment.
Computer synthesis has 2 main textures:
Filtered pink noise to provide backing texture
Modified FM synthesis to provide accompaniment to the soloist
Music alters between different styles to encourage a variety of performance movements.
Wide tempo variety helps encourage a non-identical performances.

## Slide 30
Ethereal Presence opening page
Adam Cope- Cyberinet

## Slide 31: Computer Processing

## Slide 32: Processing/Manipulation in Max
The main goal of the Cyberinet is to collect and transmit the sensor data.
From there it is largely up to the user to decide what they want to to with the data.
To help with that I have also created a series of Max patches that can be used to control various elements of a Max patch including:
Reverb
Various Delays
Gain
Debug testing tool
Tuner
Playback Control
DMX Control
More coming soon!

## Slide 33: Max Patches Continued
CNET.receive receives all the data from the Cyberinet, sorts and scales it for use, then outputs the numbers to unique object outlets.

## Slide 34
CNET.receive
Notes: Implement the CNET.receive object to utilize Cyberinet in any max patch.

## Slide 35
CNET.recieve patch inner workings

## Slide 36: Sending data to other programs
Data from the Cyberinet can be read by any Serial Monitor.
Data is formatted for Max by default.
Programs like Max can then convert the messages to different formats and transmit them to other devices and software as needed.

## Slide 37: Online Resources

## Slide 38: Github Repo
Contains all code, diagrams, and other information
github.com/mbardin/Cyberinet

## Slide 39: Code, Patches and Diagrams
Cyberinet units will be available for purchase at a future date.
All materials are open-source.
A person can build their own unit using the online resources

## Slide 40: Music

## Slide 41: Raindrops on a Tin Roof (2022-2023)
Utilizes all the included sensors:
Gyroscope/Accelerometer
Airflow
Buttons
The performer cues up various sound files and musical sections using the buttons.
Other sensors are used to control the processing of the sounds.
Sounds range from relaxing to extremely chaotic.
Text by Matthew A. Bardin

## Slide 42
Raindrops on a Tin Roof
opening page
Adam Cope - Cyberinet
Matthew Bardin - Narrator

## Slide 44: Future Directions

## Slide 45: Potential Future Directions Include:
Optimal serial communications for Windows and Mac operating systems.
Completing and refining the options for expansion units.
OSC Formatting for easier multi-platform use cases.
Permanent embedding within a clarinet.
Making versions for other instruments.
Password locking units to avoid miss-connections.

## Slide 46: Final Notes

## Slide 47: All the compositions are available in Max.
Each of the patches used to make these performances has been created as an object in Max. Performers can download these from the GitHub repo for performance, or experiment with their own processing.
46
Scores, patches and other info available at matthewbardin.com

## Slide 48: Questions?

## Slide 49: Thank You for coming!