## Slide 1: Working with the Cyberinet
Matthew A. Bardin (2023)

## Slide 2: Cybernetic + Clarinet

## Slide 3: Why use this?
The Cyberinet is a sensor array designed to be easily adapt the instrument for electronic music without impeding the performance of the instrument.

## Slide 4
Main Unit Prototype
Bottom
Top

## Slide 5
Button Board prototype

## Slide 6: Components included
The main Cyberinet is comprised of a main unit and smaller secondary unit.
Main Unit:
Lithium Ion battery to power the device.
TP-4056 board. (controls the charging and power distribution
MPU-6050 board. (6 axis gyroscope and accelerometer)
SDP-31 board. (measures air pressure and temperature)
ESP-32 DEVKIT board. (microcontroller and transmitter)
2 programmable LEDs.
Secondary Unit:
2 momentary switches with independently programmable LEDs

## Slide 7
Version 1 Components

## Slide 8
Main Unit and Button Board PCB Diagrams

## Slide 9: Optional add-ons
To further expand the functionality of the Cyberinet, multiple optional expansion units contain a variety of other sensors and can be utilized through the same expansion port. These include:
Microphone
Finger pressure sensors
Secondary movement sensor
Speaker
All of these are still in development, with the microphone closest to being functional.

## Slide 10: Music

## Slide 11: Puzzle of a Park (2023)
Written to utilize the optional button add-on.
Performer triggers the on-stage microphone & playback of recordings with a single button.
Functions similarly to a loop pedal.

## Slide 12
Ethereal Presence opening page

## Slide 13: Assembling the Unit
Attach LEDs and Resistors with Toaster Oven
Solder the larger chips directly to the main PCB. This keeps the main unit as thin as possible.
Attach the connectors to the main board. These are connected by ribbon cables and are supported by the outer case itself.
Add a power switch in between the battery and the charging port.

## Slide 14
Version 1 with Button Board (with and without housing)

## Slide 15: How it works

## Slide 16: Collects data
The Cyberinet’s .ino code and attached sensors manage the collection of the performance data.
SDP31: Measures differential air pressure between the inside and outside of the instrument. Small tubes connect to the sensor to facilitate this. Also measures temperature.
MPU6050: Measures performer movement in 6 axis.
Buttons: triggerable by the performer

## Slide 17: Transmits wirelessly
The main unit’s ESP-32 board the transmitting as well as the data collection.
By including the Arduino library “BluetoothSerial” the DEVKIT can transmit serial communications through a bluetooth connection. The device name is “Cyberinet V1.x” and currently requires no password to connect.

## Slide 18: Music

## Slide 19: Ethereal Presence (2022)
Utilizes gyroscope and airflow sensors
As the performer moves, the position of their instrument changes the pitch content of the accompaniment.
Computer synthesis has 2 main textures:
Filtered pink noise to provide backing texture
Modified FM synthesis to provide accompaniment to the soloist
Music alters between different styles to encourage a variety of performance movements.
Wide tempo variety helps encourage a non-identical performances.

## Slide 20
Ethereal Presence opening page

## Slide 21: processing/manipulation in Max
The main goal of the Cyberinet is to collect and transmit the sensor data.
From there it is largely up to the user to decide what they want to to with the data.
To help with that I have also created a series of Max patches that can be used to control various elements of a Max patch including:
Reverb
Delay
Gain
Band-Pass Filter
Playback Control
More coming
These are the Max patches I am using in the creation of a handful of music utilizing the Cyberinet in addition to other requested patches.

## Slide 22: Max Patches Continued
The main 2 max patches included in the library are the two different receive patches.
The 2 patches work to receive and process the data coming in from the Cyberinet.
Cyberinet.Omnireceive is receiving, mapping, and outputting ALL of the sensor data at the same time.
Cyberinet.receive is technically receiving all of the data, but filters out all but one of the sensors and only outputs the selected output.

## Slide 23: Sending to other programs
Data from the Cyberinet can be read by any software capable of receiving Serial data.
Simply connect the Cyberinet to the host computer and use the software’s ability to read serial data.
Another option is to send the data to Max as shown then transmit the data via OSC. This can be useful for processing data and sending it to other devices since the Cyberinet can only be connected to one host device at a time.

## Slide 24: Online Resources

## Slide 25: Github Repo
Contains code, diagrams, and other information
github.com/mbardin/Cyberinet

## Slide 26: Code, Patches and Diagrams
All the resources are available on the GitHub repo.
If you would like to program your own unit, the base Arduino code and the necessary libraries are provided.
The Max patches used in my compositions as well as just the main receive patch is provided here as well. I am working to make a library that includes a lot of options for using the data.
Part lists, circuit diagrams, etc. are all available as well. I’m planning to sell these when complete, but if you want to make one yourself, I’ll have everything listed here. I’m unsure if I will offer it as a kit or not.

## Slide 27: Future Directions

## Slide 28: Future directions include
Password locking units to avoid miss-connections
Permanent embedding within a clarinet?
Survey about potential expansions/patches?
Making versions for other instruments.

## Slide 29: All the compositions are available in Max.
Each of the patches used to make these performances has been created as an object in Max. Performers can download these from the GitHub repo for performance, or experiment with their own processing.
28
Scores, patches and other info available at matthewbardin.com

## Slide 30: Questions?

## Slide 31: Music

## Slide 32: Raindrops on a Tin Roof (2022-2023)
Utilizes all the included sensors:
Gyroscope/accelerometer
Airflow
Buttons

## Slide 33
Raindrops on a Tin Roof opening page